## Slide 1: F.I.T. Machine shop
Re-Certification

## Slide 2
Day 1
  Language spoken in shop
We speak in thousands of an inch.
.001 = one thousands
.010 = ten thousands
.100 = one hundred thousands

## Slide 3
How is .375 communicated in the shop?
.490?
1.514?

## Slide 4
All metric dimension's should be translated into English or thousands.
_____mm/ 25.4 =_______
Divide metric dimension by 25.4 to get translation to English dimension.

## Slide 5
Examples
6 mm / 25.4 = .2362
12 mm / 25.4 = .4724

## Slide 6
Nomenclature of a dial caliper

## Slide 7
Outside Diameter
Hole Depth
Step Distance
Inside Diameter
4 ways to use

## Slide 8
Dial calipers
Every line is >l l< .001 on dial.
Every complete revolution from 0 to 0 is .100

## Slide 9
1” inch is made up of 10
(.100 thousands)

## Slide 10
Dial calipers
How would we say this dimension on the caliper?

## Slide 11
Three inches, one hundred seventy five thousands.
or
3.175
Other Examples
1/4 = .250
3/8 = .375
1/2 = .500

## Slide 12
Understanding

## Slide 13
English
Metric

## Slide 14
¼ (.250)
major diameter
20 THREADS PER INCH
(TPI)
English

## Slide 15
AJORM
8mm
Major Diameter
1.25 mm
Thread Pitch
Metric

## Slide 16
Tap drill sizes

## Slide 17
Clearance drill sizes
Clearance holes have to be larger than major diameter of thread
The proper clearance hole for a ¼-20 bolt is .281 diameter.

## Slide 18: Remember when drilling a hole always: peck Drill, drilling in steps and withdrawing the tool and always use spray coolant

## Slide 19: When using vertical band saw: Lower the blade guard to with in ¼ inch of part Use push block on round parts use a vise to hold part from turning

## Slide 20: Always use proper sized vise that is hand held

## Slide 21: Always wait for machines to stop turning before removing parts

## Slide 22: Miter saw is best used for parts long enough to securely hold while keeping safely from turning blade

## Slide 23: Reading a steel rule

## Slide 24: This is a drawbar which tightens the tools into the collet on the milling machine

## Slide 25: An edge finder is used to establish center line relative to a surface

## Slide 26: .200 of inch diameter
When the edge finder kicks out, the center of the spindle will be at .100 inch away from edge of part.

## Slide 27: Micrometers are the most accurate way to measure in our shop

## Slide 28: The Tool post is where all lathes tools are mounted

## Slide 29: To make the belt driven motor go faster move belt to larger diameter groove on the motor side

## Slide 30: Milling machine coordinates

## Slide 31: Fixed jaw moveable jaw

## Slide 32: The rate The spindle turns on a machine is speed

## Slide 33: The rate of movement of the cutting tool into the workpiece is known as feed

## Slide 34: Long hair must be tied back No dangling necklaces No flip flops or open toed shoes long sleeves rolled up

## Slide 35
Review Drawing

## Slide 39
Remember!
1) Come see us before using equipment
2) Bring in drawings for review
3) After working always cleanup and put away tools

## Slide 40
Watch Safety Video
http://media.fit.edu/load.php?clipid=5924

## Slide 41
Congratulation's you are certified!

## Slide 42
Shop Tour
Demo Miter Saw
Demo cutting round stock on band saw
Demo how to sign in with I.D.
Eye wash Station
First Aid Kit