## Slide 1
  Ground Mission: Configuration Demonstration
    Timed mission to demonstrate efficiently changing mission configurations.
    Parking configuration shall not exceed 2.5 ft across the wingspan.
MISSION STATEMENT
MISSION REQUIREMENTS
Specifications:
  Empty Weight: 8.1 lbs
  Carbon Fiber Fuselage Stringers
  Laser Cut Wood Frame
  Hotwire CNC Cut Foam Wing
  3D Printed Mounts
Design Methodology:
Rapid on-site repair capability
Mission adaptability
Semi-monocoque fuselage and tail design
Detachable wing mechanism to optimize spatial efficiency
M1: Delivery Flight
3 Laps in 5 minutes
20 ft Takeoff
Payload: Pilots
M2: Medical Transport Flight
3 Timed Laps with Weighted Cabinet
Payload: Weighted Medical Supply Cabinet, 2 EMTs, Patient, Gurney, and Pilots
M3: Urban Taxi Flight
Maximum laps in 5 minutes
Payload: Passengers and Pilots
Two 4s LiPo Batteries
Max Thrust: 12.5 lbf
Flight Duration: 9 minutes
Prop Size: 13” x 6.5”
Table 1: Aerodynamics Data
AERODYNAMICS SUBSYSTEM
STRUCTURES SUBSYSTEM
ELECTRONICS SUBSYSTEM
AIAA – Design, Build, Fly (DBF)
Team Members: MK Shultz, Nicolas Street, Kanon Hotta, Jordan Tibbetts, Anas Alhubayshi, Abdullah Alanazi, Nawaf Aldhawyan, Ibrahim AlMurdhimah, Hussain Maqbul​
Faculty Advisors: Dr. Ratneshwar Jha and Dr. Eric Swenson, Dept. of Aerospace, Physics, and Space Sciences, Florida Institute of Technology
ACKNOWLEDGEMENTS
Figure 5: Complete CAD Model
Figure 2: Electronics Layout
Figure 3: Fuselage Structure
Figure 4: Tail Structure
AIAA - DBF aims to design a remote-controlled aircraft that complies with 2024 AIAA-DBF competition rules centered around Urban Air Mobility applications. The project focuses on designing, fabricating, and testing a scale aircraft that meets competition requirements while incorporating innovative design principles.
We extend our gratitude to Felix Gabriel, Zac Gross, and the staff at the L3Harris Design Center for their invaluable support. The team also expresses appreciation to our GSA, George Nehma, and Mattea Cheung, who has volunteered her time to this project.
Figure 1: Aerodynamics Analysis
Cruise Speed | 30​ mph
Alpha @ T/O | 12.5°
CL | 1.585​
CD | 0.225
CL/CD | 7.029