## Slide 1
Summary
Stability Analysis through Bipropellant Engine Research (SABER) is a small-scale, compressed air and propane bipropellant rocket engine designed as the test subject of a combustion instability analysis. Through various static fires at varying combustion chamber lengths, the project demonstrates that less combustion instabilities are experienced at smaller characteristic lengths.
Testing System
The test stand consists of four components: the static coupler which is 16.50 in tall , the dynamic coupler which is 8.875 in, the gussets, and a base plate which has a diameter of 16 in.
The data acquisition system was used to aid in our combustion instability studies. This DAQ measured pressure, temperature and thrust through a PCB.
Fluids System
Structures System
Engine Design and Analysis
Testing & Validation
SABER – Stability Analysis through Bipropellant Engine Research
S. Conley, R. Gaulin, E. Lucas, A. Ramirez, N. Reese, W. Reinkoester, J. Sadler, W. Tinelli, B. Varozza
Faculty Advisor: Dr. Firat Irmak, Dept. of Aerospace Engineering, Florida Institute of Technology
Conclusions
Combustion instabilities increase as the characteristic length decreases.
Minimizing combustion instabilities contributes to safer, more efficient engines.
Engine safety is important as there is an increase in manned missions.
The SABER team thanks our faculty advisor, Dr. Firat Irmak, our graduate student assistant, Niall Harris, and the Florida Tech L3HSDC staff.
Impact and Future Work
The bipropellant engine designed serves as a test bed for a combustion instability analysis – enabling further research into methods to reduce combustion instabilities and contribute to safer space vehicles. The project works to expand Florida Tech's ability to research various propellants and engine geometries. Future works include optimizing mass for a flight configuration.
Injector: triplet impinging jet with mutually perpendicular elements, ox-fuel-ox, utilizes a plate system and was manufactured from Al-6061 using a 3- and 3.5-axis CNC mill.
Combustion Chambers and nozzle manufactured on the manual lathe using mild steel with 2.0 FOS.
Oxidizer hose travels from an air tank to the injector's oxidizer intake.
Fuel hose travels from a propane tank to the injector's fuel intake.
2 solenoids connect to the controller, allowing propane and air-flow control from a distance.
2 ball valves are placed between the solenoids and propellant tanks, allowing for manual fluid control.
Pneumatic Tests
Verify structural integrity and that system is leakage free by pressurizing full system to 200 psia using an air compressor.
Hydrostatic Tests
Verify structural integrity and that system is leakage free by pressurizing full system to 200 psia using a pump and water.
Concept of Operations
    Static Fire Tests
    Verify engine can produce thrust and gather relevant data for instability analysis.
Static Coupler
Pre-Ignition
Gussets
Ignition
Cool Down
  Connect DAQ
  Fill propane tank from reservoir
  Fill air compressor tank
  Connect feed lines
  Open ball valves
  Verify safe distance
  Light igniter
  Open fuel solenoid
  Open ox solenoid
  Monitor burn until flame burnout
  Close solenoid valves
  Wait for system to cool down
  Disconnect feedlines
  Save recorded data on DAQ
Injector
Combustion Chamber
Nozzle
Dynamic Coupler
The engine is made of three main components: a multi-plate impinging injector, a combustion chamber which varies in length throughout the study, and a C-D nozzle.
Chamber Inner Dia.: 2.5 in
Chamber A Length: 3.686 in
Chamber B Length: 2.738 in
Chamber C Length: 1.789 in
Oxidizer Inlet
Fuel Inlet
Fuel Manifold
Oxidizer Manifold
Gaskets
Velocity CFD of
combustion chamber A.
Solenoid
Solenoid
Ball Valve
Ball Valve
Propane Tank
Air Tank and Compressor
Air Hose
Propane Hose
Acknowledgements